## Slide 1
Comparative Performance Analysis of TCP Congestion Control and SDN Controllers
Level A Project - COP 5718 Network Performance Analysis

## Slide 2
Project Overview & Goals
Objective: Compare performance of TCP congestion control algorithms (Reno vs CUBIC) and UDP across two SDN controllers (POX vs Ryu)
Topology: Dumbbell network with 22 hosts, 6 switches, 2 routers, and a 10 Mbps bottleneck link
Performance Metrics: Throughput, Latency, Packet Loss, Jitter
Project Level: A (3 Wild Cards achieved)
✓ Compare 2 SDN controllers (POX vs Ryu)
✓ Compare 3 protocols (TCP Reno, TCP CUBIC, UDP)
✓ Compare 4 performance statistics

## Slide 3
Why These Protocols?
TCP Reno:
• Classic congestion control algorithm
• Fast recovery with fast retransmit
• Baseline for comparison
TCP CUBIC:
• Modern cubic window growth function
• Better for high-bandwidth, high-latency networks
• Default in Linux kernels since 2.6.19
UDP:
• Connectionless, no congestion control
• Maximum throughput potential
• Reveals network capacity limits
Why Compare?
• Understand congestion control impact
• Evaluate modern vs classic algorithms
• Assess protocol behavior under stress

## Slide 4
Why These SDN Controllers?
POX Controller:
• Python-based, OpenFlow 1.0
• Single-threaded, simpler architecture
• Widely used for research and education
• Easier to debug and understand
Comparison Goal:
• Evaluate controller overhead impact
• Compare protocol implementations
• Assess forwarding efficiency
Ryu Controller:
• Python-based, OpenFlow 1.3+
• Multi-threaded, modern design
• Component-based architecture
• Production-grade performance
Why Not ONOS?
• Connectivity issues (5/7 switches)
• Excessive convergence time (>120s)
• Inconsistent switch registration

## Slide 5
Why Dumbbell Topology?
Network Design: 22 hosts, 6 switches, 2 routers with bottleneck link
Bottleneck Configuration:
• 10 Mbps bandwidth (intentionally limited)
• 50 ms propagation delay
• 1% packet loss rate
Advantages:
• Simulates real-world congestion scenarios (ISP peering points, WAN links)
• Forces congestion control mechanisms to activate
• Clear separation of access and core network
• Enables controlled comparison of protocol behavior under stress

## Slide 6
Results: Throughput Analysis
[Insert Figure Here]
Key Findings:
UDP achieved highest throughput (~20 Mbps) but with 52% packet loss
TCP CUBIC outperformed TCP Reno across both controllers
POX showed marginally better throughput than Ryu for TCP protocols
All TCP variants stayed within bottleneck limits (10 Mbps)

## Slide 7
Results: Latency Analysis
[Insert Figure Here]
Key Findings:
All configurations showed similar latency (~50 ms)
Dominated by configured propagation delay in bottleneck link
Minimal controller overhead impact
TCP vs UDP showed negligible latency differences

## Slide 8
Results: Packet Loss Analysis
[Insert Figure Here]
Key Findings:
UDP: ~52% packet loss (no congestion control)
TCP Reno-POX: ~4% packet loss (highest among TCP)
TCP CUBIC-Ryu: ~3% packet loss
TCP protocols effectively managed congestion
CUBIC's window growth showed better adaptation

## Slide 9
Results: Jitter Analysis
[Insert Figure Here]
Key Findings:
POX demonstrated lower jitter than Ryu
Suggests more consistent packet scheduling in POX
Ryu's multi-threaded architecture introduced timing variability
UDP jitter measurements affected by Ryu's inconsistent delivery patterns

## Slide 10
Key Findings & Conclusions
TCP CUBIC is the clear winner for congestion-prone networks
• Better throughput than Reno, lower packet loss
• Modern cubic window growth function adapts effectively
POX provides marginally better performance for our use case
• Lower jitter, slightly better TCP throughput
• Simpler architecture beneficial for controlled experiments
UDP demonstrates fundamental tradeoff:
• Maximum throughput when no congestion control
• Unacceptable packet loss (52%) in congested networks
Controller choice matters less than protocol design

## Slide 11
Live Demo Structure
Each team member will demonstrate:
Member 1: Topology setup and network creation
• Run simple_dumbbell.py to create network
• Verify host connectivity and switch registration
Member 2: Experiment execution
• Run automated experiment scripts
• Show real-time iperf3 throughput measurements
Member 3: Results analysis and visualization
• Generate performance graphs from collected data
• Demonstrate analysis pipeline